## Slide 1: Topic 6 – Intermodal Transportation and the Container
A – Intermodalism
B – Containerization

## Slide 2: A – Intermodalism
Read section 1

## Slide 3: Intermodalism and Transmodalism
Read this content
Origin
Destination
Road
Rail
Maritime
Rail
Rail
Ticket / Contract
Ticket / Contract
Ticket / Contract
Ticket / Contract
Terminal
Carrier
Intermodalism
Multimodalism
Transmodalism

## Slide 4: Integrated Freight Transport Systems: Intermodal and Transmodal Connectivity
Distribution Center/ Cross-docking
Transloading facility
On-dock
rail
Port container yard
Thruport
Transshipment Hub
Road
Rail
Maritime
Intermodal Connectivity
Transmodal Connectivity
Read this content
What are the fundamental differences between intermodal and transmodal transportation?

## Slide 5: Modal Separation in Space: Europa Terminal in Antwerp
Trucks
Deepsea services
Rail
Barges
Read this content
Notes: Source: Terminal photo from PSA Antwerp.

## Slide 6: Abu Dhabi, Major Transshipment Hub

## Slide 7: Rail / Road Transloading
Read this content

## Slide 8: Major Steps in Intermodal Integration
Read this content
Pallets
Forklifts
TOFC (1952)
Container (1956)
Container terminal (1962)
Container standardization (1965)
Transatlantic services (1966)
COFC (1967)
Cellular containership (1968)
Container gantry crane and
straddle carrier (1959)
Satellite terminals
Inland container depots
Automated terminal (1995)
Post-Panamax ship (1996)
New-Panamax (2014)
Blockchain (2015)
MGX-24 (2019)
Electronic bill of lading
Advanced container
Inventing Intermodalism
Intermodal Standards
Operationalization
Massification and Automation
1930s
1940s
1950s
1960s
1970s
1980s
1990s
2000s
2010s
Rail deregulation
Rubber-tired gantry (1985)
Reachstacker (1985)
Doublestacking (1985)

## Slide 9: Pallets Loaded into a Train by a Forklift, 1940s

## Slide 10: Trailers on Flatcars (TOFC), 1950s

## Slide 11: What is a Container?
A standard metal box (ISO 668 standard)
  20-foot box of 20 feet long, 8'6" feet high and 8 feet wide (One TEU; Twenty Foot equivalent Unit).
  40-foot box (equals two TEU).
  40-foot ‘high cube’ box. 9’6” feet high (often counted as two TEU).
Using common handling equipment
  Moving between ships, railcars, trucks and barges.
The container is a load unit
  Can be adapted to carry different cargoes.
  Standard: General dry cargo.
  Tank: Liquid cargo (fuel and chemicals).
  Reefer: Refrigerated cargo (food).

## Slide 12: First Containership, Port Newark, 1958

## Slide 13: Cellular Containership, 1970s

## Slide 14: Containers on Flatcars, 1978
Doublestacking

## Slide 15: Automated Guided Vehicles, Container Yard, HHLA Container Terminal Altenwerder (CTA), Hamburg

## Slide 16: Conditions for Intermodal Transport
Explain under what conditions intermodal transportation is used.
Read this content
CONDITIONS
OUTCOMES
X
Load unit
Modal continuity
Transport distance
Cargo Value
Frequency of shipments
Total transport costs
Intermediate and finished goods in load units of less than 25 tons.
Sequence of connected infrastructure; an intermodal transport chain.
Distances above 500 km (longer than one day of trucking) usually require intermodal transportation.
Suitable for intermediate cargo values. Low and high value shipments are usually less suitable.
Cargo flows need to be continuous and in similar quantities.
From economies of scale and the use of more effective modes and intermodal operations.
Modal shift
Each mode according to their respective time and cost advantages.
Consolidation
Requirement to consolidate and deconsolidate load units at intermodal terminals.
Higher load factor
Less LTL and more TL. Better utilization of existing capacity.
Less empty backhauls
Less vehicle-km of empty backhauls due to modal shift, higher load factor and consolidation.

## Slide 17: Unimodal and Intermodal Transportation
Explain how an integrated intermodal network can be a more efficient form of transportation.
Read this content
A
C
D
F
E
B
A
C
D
F
E
B
Rail
Road
Transshipment
Transshipment
Intermodal Integrated Network
Unimodal Point-to-Point Networks

## Slide 18: Distance, Modal Choice and Transport Costs
Read this content
Distance
Transport costs per unit
D1
D2
C1
C2
C3
ROAD
RAIL
MARITIME

## Slide 19: Freight Transport Revenue per Ton-Mile (in 2006 dollars)
Chart: 
| Water | Rail | Road | Air
2006 | 0.007 | 0.02 | 0.27 | 0.8
Read this content
Notes: Source: U.S. Department of Transportation, Bureau of Transport Statistics, National Transportation Statistics, 2009.

## Slide 20: Average Length of Haul, Domestic Passenger and Freight Transport, United States, 1960-2019 (in miles)
Chart: 
| 1960 | 1965 | 1970 | 1975 | 1980 | 1985 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
Air carrier (cargo) | 953 | 943 | 1014 | 1082 | 1052 | 1157 | 1389 | 1307.1148 | 1496.482 | 1478.3477 | 1579.6703 | 1554.6118 | 1441.2093 | 1115.4654 | 1104.8652 | 1054.5521 | 1076.6812 | 719.5544 | 1204.4432 | 1197.2121 | 1240.783 | 1218.4401 | 1218.129 | 1219.6836 | 1245.7862 | 1161.5024 | 1156.9672 | 1150.4756 | 1174.4044 | 1152.8416 | 1161.457 | 1165.1672 | 1166 | 1202 | 1217 | 1212
Truck | 272 | 259 | 263 | 286 | 363 | 366 | 391 | 398 | 410 | 407 | 392 | 416 | 426 | 435 | 442 | 458 | 473 | 485
Class I Rail | 461.3 | 503 | 515.1 | 540.7 | 615.8 | 664.5 | 725.7 | 751.3 | 762.5 | 794.2 | 816.8 | 842.5783 | 841.7285 | 850.9264 | 835.1011 | 834.9323 | 843.2894 | 858.4962 | 853.023 | 862.3575 | 901.5271 | 893.4567 | 905.613 | 912.7753 | 919.0543 | 918.4537 | 913.5644 | 917.1646 | 973.207 | 990.349 | 1006.0191 | 1019.9647 | 1021 | 1033 | 1046 | 1032
Coastal | 1496 | 1501 | 1509 | 1362 | 1915 | 1972.2 | 1604.6001 | 1705.0357 | 1761.8765 | 1650.3651 | 1651.9881 | 1651.7071 | 1526.126 | 1329.6959 | 1261.474 | 1279.4143 | 1251.0868 | 1227.9016 | 1218.5222 | 1247.9584 | 1268.6179 | 1232.869 | 1125.6457 | 1108.1244 | 1115.8207 | 1170.4848 | 1169.2863 | 1119.3292 | 1032.1787 | 993.3911 | 1002.7302 | 1002.8755 | 1018 | 1073 | 1084
Air carrier (passenger) | 583 | 614 | 678 | 698 | 736 | 758 | 803 | 806 | 806 | 799 | 787 | 791 | 802 | 817 | 812 | 824 | 834.1471 | 844.5027 | 851.5391 | 844.7426 | 861.9308 | 866.0718 | 872.6486 | 872.1364 | 871.9322 | 872.0655 | 878.1907 | 883.117 | 885.4004 | 895.0113 | 898.1844 | 906.1037 | 917 | 922 | 927 | 928
Amtrak | 236 | 216 | 231 | 273 | 285 | 286 | 280 | 279 | 268 | 256 | 256 | 251 | 248 | 244 | 236.5532 | 233.6752 | 230.9405 | 218.5527 | 214.5973 | 220.3674 | 217.8606 | 215.2452 | 216.7985 | 220.2986 | 212.8483 | 217.7739 | 218.1358 | 218.1358 | 212.7365 | 208 | 205 | 200 | 198
Intercity Bus | 79 | 94 | 106 | 113 | 125 | 121 | 141 | 143 | 136 | 138 | 138 | 140 | 143 | 144 | 144 | 143 | 143
Commuter rail | 23.3 | 23.8 | 21.6 | 23.1 | 23.3 | 21.6 | 23.6 | 24 | 23.707 | 22.5014 | 22.8617 | 22.148 | 22.7727 | 22.8243 | 22.9421 | 23.3247 | 23.4726 | 22.3924 | 23.482 | 24.3139 | 23.4098 | 23.9876 | 23.4226 | 24.5277 | 23.7077 | 24.6797 | 23.8773 | 23.8268 | 24 | 25 | 25 | 25
Freight
Passengers
Read this content
Notes: Source: RITA/BTS. Table 1-38: Average Length of Haul, Domestic Freight and Passenger Modes.
http://www.rita.dot.gov/bts/sites/rita.dot.gov.bts/files/publications/national_transportation_statistics/html/table_01_38.html

## Slide 21: Modal Share of Freight Transportation, Selected Countries, 2008 (in % of ton-kms)
Chart: 
| EU27 | United States | China | Russia | Japan
Rail | 443 | 2657 | 2657 | 2116 | 3.9
Road | 1878 | 1923 | 1209 | 216 | 57.8
Pipelines | 124 | 814 | 302 | 2464
Sea | 1498 | 481 | 8450 | 84 | 36.5
Inland waterways | 145 | 472 | 1112 | 64
Read this content
Why Europe, the US and Japan have different composition of transport modes?
Notes: Source: AT Kearney
https://www.atkearney.com/documents/10192/295992/Russian_Rail-Containers-and_Growth.pdf/010bafbb-54d6-46d0-9ff9-25b53c27645c

## Slide 22: Intermodal Transport Chain
Read this content
Transfer
Local / Regional Distribution
National / International Distribution
Transport Terminal
‘First mile’
‘Last mile’
Composition
Interchange
Decomposition

## Slide 23: The North American Landbridge
Read this content

## Slide 24: The Eurasian Landbridge
Read this content
Explain how the North American and Eurasian Landbridge are examples of intermodalism.
Notes: Source: International Union of Railways (2004) The Northern East West (N.E.W.) Freight Corridor, Transportutvikling AS.

## Slide 25: Short Assignment: The Choice of a Transport Mode
Explain how distance and cost are factors in selecting a specific transport mode.

## Slide 26: B – Containerization
Read section 3

## Slide 27: The Benefits of Containerization
Read this content
The container has become a dominant mode of global freight transportation. Explain the main reasons why.
What is containerization
Transportation Costs
Inventory Costs
Service Level
Lower freight rates.
Lower insurance rates.
Minimal load unit.
Lower storage costs.
Lower packing and packaging costs.
Faster inventory turnover.
Time reliability.
Higher frequency.

## Slide 28: Container Identification System
Read this content
Check digit calculator
Owner Code (3 letters): TGH
Product Group Code (1 letter): U
Registration Number (6 digits): 759933
Check Digit (1 digit): 0
Size & Type Code (4 digits/letters): 45G1
Maximum weight: 30,480 kg
Container weight: 3,870 kg
Payload weight: 26,610 kg
Cubic capacity: 2,700 cubic feet
1
1
2
2
3
3
4
5
4
5
Operational Characteristics

## Slide 29: Common ISO Container Size and Type Codes
Read this content
2
4
L
M
20 feet
40 feet
45 feet
48 feet
2
5
8 feet 6 inches
9 feet 6 inches
“High cube”
G1
General purpose container
R1
Refrigerated container
U1
Open top container
P1
Platform container
T1
Tank container
Length
Height
Type
Notes: 1995 ISO standard

## Slide 30: Conventional Intermodal Terminal Equipment
Read this content
Circulate over container piles. Can go over stacks up to 3 in height. Density of 500 to 700 TEU per hectare.
Use container top anchor points. Handle most containers. Can reach stacks up to 3 in height.
Flexible side loaders. Can reach stacks up to 3 full or 5 empty containers in height. 500 TEU per hectare.
High storage densities (1,000 TEU per hectare). Difficult to move from one stack to the other. High acquisition but low operating costs.
Highest storage density (wide span; +1,000 TEU per hectare); mostly used at port terminals. Lowest operating costs. Fixed to rail tracks.
Load and unload containerships.
Various sizes (Panamax and Super-Panamax).
Straddle Carrier
Rubber-tired Gantry
Front-end Loader
Reach Stacker
Portainer
Rail-mounter Gantry
Straddle Carriers at ECT Delta Terminal Rotterdam
Rubber Tire Gantry Cranes working at Dublin Port

## Slide 31: Composition of the Global Fleet of Containers, 2012
Chart: 31.5 Million TEU
| 20 Foot | 40 Foot | 40 Foot High Cube | Reefer | Tank | Others
TEU | 5 | 5.9 | 15.4 | 2.1 | 0.25 | 2.7
20 Foot Containers
  Carry heavier goods.
  Running out on weight before run out of volume.
40 Foot Containers
  Carry more volume than weight.
40 Foot High-Cube
  Highest volume available in maritime shipping.
Reefer
  Carry refrigerated goods.

## Slide 32: Number of Units and Weight of Standard Consumption Goods that Can be Carried by a 20 Foot Container
Chart: 
| Copying paper | Cell phone | DVD player | Pair of shoes | Flat Screen Televisions | Wine Bottles | Bananas | Refrigerators
Units | 1650 | 12000 | 1600 | 6000 | 400 | 9600 | 48000 | 55
Payload Weight (kg) | 20388 | 8279 | 3916 | 4648 | 4680 | 12000 | 9792 | 5500
Weight Limit
Read this content
What is the difference between “weighting out” versus “cubing out” in containerized transportation?
Notes: Source: adapted from T. Toikka (2006) “The Real Price for Container Transportation between Asia and Europe”, Lappeenranta University of Technology,
Department of Industrial Engineering and Management.

## Slide 33: Palletized versus Floor Loaded Container

## Slide 34: Containerization as a Diffusion Cycle: World Container Traffic (1980-2020)
Chart: Million TEU
| 1980 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Adoption | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Acceleration | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Peak Growth | 1 | 1 | 1 | 1 | 1 | 1 | 1
Maturity | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Traffic | 38.8 | 52.7 | 57.4 | 59.4 | 67.3 | 73.8 | 78.5 | 88 | 93.6 | 102.9 | 113.2 | 128.3 | 145.5 | 158.3 | 176.5 | 190.9 | 210.5 | 224.7745 | 235.0755 | 263.4565 | 296.9961 | 338.4337 | 376.2681 | 416.752 | 489.8183 | 516.1523 | 472.273 | 560.1592 | 606.1712 | 634.2844 | 656.3287 | 687.0841 | 697.146 | 710.616 | 757.978 | 793.26 | 802 | 775
1966-1992
1993-2001
2002-2008
2009 -
Adoption
Acceleration
Peak Growth
Maturity
New (niche) services
Productivity gains
Network development
Productivity multipliers
Massive diffusion
Network complexities
Niche markets
Diffusion Level
Time
Adoption
Acceleration
Peak Growth
Maturity
© GTS
Read this content

## Slide 35: Containerization Growth Factors
Read this content
Substitution
Induced
Incidental
Derived
Capture of bulk and break-bulk markets
New niches (commodities and cold chain)
Trade imbalances
Repositioning of empty containers
Transshipment (hubbing, relay and intersection)
Economic and income growth
Outsourcing and offshoring
Complex supply chains
Economic recessions
Trade protectionism
Automation
Peak substitution
Composition of container fleet
Trade protectionism
Automation
Changes in shipping networks (more direct services)
Growth
Decline

## Slide 36: Containerized Cargo Flows along Major Trade Routes, 1995-2020 (in million TEUs)
Chart: 
| 1995 | 2000 | 2005 | 2010 | 2015 | 2020
East Asia>North America | 3.974 | 7.308 | 11.893 | 12.3 | 17.4 | 20.6
North America>East Asia | 3.535 | 3.525 | 4.479 | 6.5 | 6.9 | 6.9
East Asia>Europe | 2.4 | 4.65 | 9.326 | 13.3 | 15 | 16.9
Europe>East Asia | 2.021 | 2.461 | 4.417 | 5.7 | 6.4 | 7.2
North America>Europe | 1.691 | 1.707 | 1.986 | 2.7 | 2.7 | 2.8
Europe>North America | 1.678 | 2.694 | 3.719 | 3.2 | 4.1 | 4.8
Read this content
Why container flows are imbalanced and what happens with empty containers?
Notes: Source: UNCTAD, Review of Maritime Transport, various years.

## Slide 37: The Container as a Transport, Production and Distribution Unit
TRANSPORT
Modes and terminals.
Intermodal and transmodal operations.
PRODUCTION
DISTRIBUTION
Synchronization of inputs and outputs (batches).
Manufacturing cycles.
Flow management (time-based).
Inventory in transit (warehousing unit).
Read this content
Notes: Source: Notteboom, T. and J-P Rodrigue (2009) "The Future of Containerization: Perspectives from Maritime and Inland Freight Distribution", Geojournal, Vol. 74, No. 1, pp. 7-22.

## Slide 38: Advantages of Containerization
Read section 4
How a container is made
Loading containership
ADVANTAGES
$
Standardization
Flexibility
Costs
Velocity
Warehousing
Security & Safety
ISO standard (modes and equipment). Unique identification number and size type code.
Commodities, manufactured goods, liquids and refrigerated goods.
Low transport costs. Economies of scale at modes and terminals.
Fast transshipment operations.
Low terminal turnaround times.
Own warehouse; simpler and less expensive packaging. Stacking capability.
Contents unknown to carriers. Reduced spoilage and losses.

## Slide 39: Drawbacks of Containerization
Illicit shipments and the response of the Container Control Programme
DRAWBACKS
$
Large consumption of terminal space. Draft issues with larger containerships.
Site constraints
Capital intensiveness
Container handling infrastructures and equipment are important investments.
Stacking
Complexity of arrangement of containers, both on the ground and on modes.
Repositioning
Theft and losses
Illicit trade
Divergence between production and consumption; repositioning. 20% of all containers.
High value goods vulnerable to thefts, particularly between terminal and final destination.
Illicit trade of goods, drugs and weapons, as well as for illegal immigration.

## Slide 40: Container Usage during its Life-Span
Chart: 
| Ocean Transit | Terminal | Inland Use | Repair | Idle or Empty Repositioning
Column1 | 16 | 16 | 6 | 6 | 56
Read this content
Notes: Source: adapted from Crinks, P. (2000) Container Usage Asset Management in the Global Container Logistics Chain, International Asset Systems. http://www.interasset.com/docs/AssetManagementWP.pdf

## Slide 41: Stacked 40-Foot Containers, Port of Yantian, China
Read this content

## Slide 42: Loading Coffee into Containers, Cartagena, Colombia
Read this content
Why a commodity such as coffee is carried in containers?
Notes: Source: Cartagena Port Authority.

## Slide 43: Floor Loaded Container with Chinese Retail Goods

## Slide 44: 40-Foot Containers Doublestacked on a Rail Car
Read this content
Notes: Source:

## Slide 45: 40’ Reefer Container

## Slide 46: 20-Foot Tank Containers
Read this content
Notes: Photo: Dr. Jean-Paul Rodrigue, 2010

## Slide 47: The Ultimate “Kegger”

## Slide 48: Reuse of a Discarded Container (South Africa)
Read this content
Discarded containers have many uses. Searching to web, provide some examples about how containers can be reused.

## Slide 49: Containerized Housing Units, Le Havre, France
Read this content

## Slide 50: Container Turned in a Swimming Pool…

## Slide 51: Short Assignment: “The World in a Box”
The container has several advantages and drawbacks. Provide a succinct explanation of the advantages and drawbacks you think are the most important.